## Slide 1
  Processor: L106 32-bit RISC microprocessor core based on the Tensilica Xtensa Diamond Standard 106Micro running at 80 MHz
  64 KiB of instruction RAM, 96 KiB of data RAM
  External QSPI flash: 512 KiB to 4 MiB* (up to 16 MiB is supported)
  IEEE 802.11 b/g/n Wi-Fi
    Integrated TR switch, balun, LNA, power amplifier and matching network
    WEP or WPA/WPA2 authentication, or open networks
  16 GPIO pins
  SPI
  I²C (software implementation)
  I²S interfaces with DMA (sharing pins with GPIO)
  UART on dedicated pins, plus a transmit-only UART can be enabled on GPIO2
  10-bit ADC (successive approximation ADC)